## Slide 1
PHOENIX
Drone Search & Rescue System
AI-assisted ground control for live drone missions.
Live Video
Drone camera stream
AI Detection
Human + thermal alerts
GPS Map
Real-time tracking
1/25

## Slide 2
Problem
Search & rescue teams need faster field awareness
Dangerous Areas
Rescuers cannot quickly enter collapsed, flooded, or unstable zones.
Limited Visibility
Ground teams miss victims hidden by distance, smoke, or terrain.
Slow Decisions
Manual searching delays mission coordination and victim detection.
Goal: turn drone data into instant, actionable rescue information.
2/25

## Slide 3
Solution
A mobile ground control station for rescue missions
Raspberry Pi
GPS + Camera
Telemetry
Firebase
Auth + Firestore
Live streams
FastAPI Server
TCP receiver
AI pipeline
Flutter App
Video + Map
Controls
One app for video, map, telemetry, reports, and control
Laptop server handles streaming and AI processing
Firebase keeps GPS/status updates live and reliable
3/25

## Slide 4
App Entry Point
Splash screen and startup decision
PHOENIX
loading app state
Initialize
Firebase + services
Check Session
Firebase user + local flag
Route
onboarding/auth/home
First screen controls the user journey
Decides whether to continue to onboarding, authentication, or home
4/25

## Slide 5
Onboarding Flow
Introduce the rescue system before login
INTRO
rescue mission value
FEATURES
video | map | AI
GET STARTED
continue
Purpose
explain search & rescue value
Capabilities
video, map, AI, control
Page Indicator
multi-page intro
Next Step
send user to sign in
5/25

## Slide 6
Authentication
Secure access before mission control
SIGN IN
email + password
GOOGLE
social login
RESET
forgot password
Sign Up
email verification
Sign In
Firebase Auth
Recovery
reset password
User Document
created in Firestore after auth success
Local Session
shared preferences login state
6/25

## Slide 7
Mobile App
Flutter ground control interface
LIVE FEED
AI Overlay active
STATUS
Battery 82% | Alt 34m
REPORTS
2 humans detected
human 92%
Dashboard
Live Map
Full Video
7/25

## Slide 8
App Architecture
Feature-first clean structure
Core
DI | Router
Theme | WS
Auth
Firebase Auth
Google sign-in
Drone
Map | Video
Telemetry
Onboarding
Splash
Intro flow
Domain
Models + repository contracts
Data
Firebase + WebSocket implementations
Presentation
Screens + Cubits + widgets
8/25

## Slide 9
System Block Diagram
Main components and communication paths
Raspberry Pi
GPS + Camera
Telemetry
Firebase
Auth + Firestore
Live streams
FastAPI Server
TCP receiver
AI pipeline
Flutter App
Video + Map
Controls
GPS / Status
Firestore stream
TCP video
WebSocket
Commands
9/25

## Slide 10
Data Flow
Separate paths for speed and reliability
GPS
lat/lng/status
Firebase
snapshots
Flutter Map
marker + path
Camera
JPEG frames
FastAPI
AI process
Flutter Video
live feed
Commands
joystick -> server
10/25

## Slide 11
Live Map
GPS tracking with path history
Firestore location stream
OpenStreetMap tiles
Path history
Disconnect handling
Last known position
11/25

## Slide 12
Map Data Source
How GPS reaches the user interface
Raspberry Pi
reads GPS
Firestore
drone/location
Repository
watch stream
Cubit
emit state
Document
lat | lng | timestamp
Model
DroneLocation
UI
marker + route update
12/25

## Slide 13
Map Rendering Layers
What appears on the map
Tile Layer
OpenStreetMap base map
Polyline Layer
drone path history
Marker Layer
drone + user location
Control Layer
center on user button
13/25

## Slide 14
Tracking State Machine
How the app reacts to GPS stream changes
Initial
screen starts
Loading
subscribe stream
Active
location + path
Disconnected
last known point
10 sec timeout
Active state updates the map marker instantly
Path history grows with every new location
Disconnected state keeps the last known position visible
14/25

## Slide 15
Map Screen UX
Operational view for rescue teams
Header
mission map context
Status Bar
battery | temp | signal
Mission Card
current operation status
Start Button
send start_mission
Map is not isolated; it is part of the mission workflow
Telemetry stays visible while tracking location
15/25

## Slide 16
Telemetry Monitoring
Live status data shown beside the mission
Battery
percentage for flight safety
Altitude
current drone height
Speed
movement awareness
Temperature
system/thermal signal
Firestore
drone/status
Status Cubit
stream state
UI Widgets
cards + bars
16/25

## Slide 17
Reports & Alerts
Incident history for mission awareness
Human Detected
AI or thermal event
System Overheated
temperature warning
Mission Complete
operation event
Firestore
reports/entries
Reports Section
latest 20 entries
Rescue Team
quick review
17/25

## Slide 18
Mission Workflow
From planning to active operation
Plan
choose target area
Start
send start_mission
Monitor
map + telemetry
Detect
AI alerts
Control
joystick commands
Review
reports log
The current app already sends start_mission
Mission planner can later add routes, zones, and waypoints
18/25

## Slide 19
Video Feed
Normal, Thermal, AI Overlay
human 92%
Normal
raw camera view
Thermal
heat-focused mode
AI Overlay
boxes + confidence
19/25

## Slide 20
Drone Control
Virtual joystick command flow
human 92%
Joystick
x/y offset
WebSocket
/ws/commands
Server
handle command
move: x/y direction
neutral command on release
ready for land / return / stop
20/25

## Slide 21
Hardware Layer
Drone onboard module
GPS Module
live location
Camera
video frames
Sensors
battery/temp
Raspberry Pi
data relay
Writes location/status to Firebase
Streams camera frames to laptop server
Ready for thermal camera integration
21/25

## Slide 22
Backend Server
FastAPI middleware on laptop
TCP Receiver
frames in
Queue
async buffer
AI Pipeline
detect + draw
Encoder
JPEG bytes
WebSocket
broadcast
/ws/video
Processed frames
/ws/detections
JSON boxes
/ws/commands
Control input
22/25

## Slide 23
AI Detection
Human detection and thermal-ready pipeline
human 92%
Frame
camera input
YOLO
human boxes
Thermal
hot spots
Overlay
HUD output
Dummy fallback keeps demos running
Final model can replace detector module
23/25

## Slide 24
Feature Challenges
Problems we faced and how the code solves them
Splash/Auth
Challenge: startup routing.
Solution: Firebase + local session check.
Map Tracking
Challenge: live GPS dropouts.
Solution: stream state + last known position.
Video Latency
Challenge: heavy frames.
Solution: TCP/WS path separate from Firebase.
AI Detection
Challenge: model availability.
Solution: detector module with fallback.
Drone Control
Challenge: continuous joystick input.
Solution: x/y commands and neutral on release.
Team Integration
Challenge: app/server/Pi sync.
Solution: clean Firestore + WebSocket contracts.
24/25

## Slide 25
THANK YOU
Questions?
Phoenix Drone Search & Rescue System
25/25