## Slide 1
PHOENIX
Drone Search & Rescue System
Graduation Project | Computer Engineering
A three-tier ground control system integrating drone hardware, AI-powered human detection, and real-time mobile monitoring for autonomous Search & Rescue operations.
Mahmoud Dahy | Supervised by: Dr. ...

## Slide 2
Agenda
Presentation Outline
01 Problem Statement & Motivation
02 Project Objectives
03 System Architecture Overview
04 Hardware Components (Raspberry Pi Module)
05 Backend Server (FastAPI & AI Pipeline)
06 AI Detection Engine (YOLO Integration)
07 Mobile App – Ground Control Interface
08 Key Features: Video, Map, Telemetry, Joystick
09 Technology Stack
10 Challenges & Solutions
11 Future Enhancements
12 Demonstration
2/24

## Slide 3
Problem Statement
The Challenge in Search & Rescue Operations
Critical delays in locating victims during natural disasters, missing person cases, and emergencies
Traditional SAR teams face limited visibility, dangerous terrain, and slow manual search patterns
Lack of real-time aerial intelligence and automated detection capabilities in the field
High cost & complexity of professional drone systems with limited accessibility for first responders
72%
of SAR operations exceed critical time windows
60%
reduction in search area coverage with aerial view
3x
faster victim localization with AI detection
3/24

## Slide 4
Project Objectives
What We Aim to Achieve
01
Real-Time Aerial Surveillance
Live video streaming from drone camera to mobile ground station with minimal latency
02
AI-Powered Human Detection
Automated identification of persons in distress using YOLO deep learning model
03
Live GPS Tracking & Navigation
Real-time drone position tracking on interactive maps with path history
04
Comprehensive Telemetry Monitoring
Battery, altitude, speed, temperature, and system health at a glance
05
Remote Drone Control
Full touch-based virtual joystick for directional drone commands
06
Mission Management
End-to-end mission lifecycle: planning, execution, incident reporting
4/24

## Slide 5
System Architecture
Three-Tier Distributed System
TIER 1
DRONE HARDWARE
Raspberry Pi Camera Module GPS (NEO-6M) Captures video & location data. Streams via TCP & Firebase sync.
TIER 2
LAPTOP SERVER
FastAPI + Uvicorn YOLO AI Detection OpenCV Processing WebSocket Server Receives drone feed, runs AI inference, broadcasts to mobile clients.
TIER 3
MOBILE APP
Flutter Ground Control Interface Live video, AI overlay, GPS tracking, telemetry, joystick control, mission management.
▶
▶
Drone → TCP Video → Laptop Server → WebSocket (Video + Detections) → Mobile App
5/24

## Slide 6
Hardware Components
Raspberry Pi Onboard Drone Module
1
Raspberry Pi
Onboard computer processing drone data & communications
(Pi 3/4)
2
Camera Module
Live video capture for aerial surveillance feed
(Pi Camera v2)
3
GPS Module
Real-time positioning data (NEO-6M) via UART
(NEO-6M)
4
Drone Frame
Quadcopter platform with payload capacity for RPi + camera + GPS
(Custom / DJI)
Data Flow: GPS Module → Raspberry Pi → TCP Socket → Laptop Server Camera → Raspberry Pi → TCP Video Stream → FastAPI Server
6/24

## Slide 7
Backend Server
FastAPI Middleware & AI Processing Pipeline
TCP Receiver (Port 9000)
Receives raw video frames from drone via TCP socket
→
Frame Queue
Buffers frames for processing at controlled rate
→
AI Pipeline (YOLO)
Resize, detect, & encode frames with bounding boxes
→
Output Queue
Queues processed frames for broadcast to clients
→
WebSocket Broadcaster
Streams video & detections to all connected mobile clients
/ws/video
Binary (JPEG)
Processed video frames at ~15-30 FPS
/ws/detections
JSON
AI detection results: bounding boxes, confidence, thermal
/ws/commands
JSON (bidirectional)
Drone control commands: move, mission, land
7/24

## Slide 8
AI Detection Engine
YOLO-Based Human Detection Pipeline
Detection Pipeline
1. Frame Capture — Extract frame from video stream
2. Preprocessing — Resize to 640×640, normalize pixels
3. YOLO Inference — Forward pass through CNN model
4. Post-processing — NMS filtering, confidence thresholding
5. Bounding Boxes — Draw detections with labels & scores
6. Encoding — JPEG encode for WebSocket transmission
Detection Features
• Real-time inference at ~15-30 FPS
• Confidence score for each detection
• Thermal mode simulation via color filters
• HUD overlay with bounding boxes & labels
• Human count tracking per frame
• Auto-generated incident reports on detection
• Fallback dummy detector for testing
8/24

## Slide 9
Mobile Application
Flutter Ground Control Interface
Live Video
Real-time MJPEG streaming with Normal, Thermal & AI Overlay modes
GPS Tracking
OpenStreetMap with drone position, path history & user location
Telemetry
Circular indicators for battery, altitude, speed, temperature & human count
Drone Control
Full-screen virtual joystick for movement, mission start/stop & landing commands
Reports
Real-time incident reports: human detected, overheat, mission complete
Authentication
Email/Password, Google OAuth & OTP verification with Firebase
9/24

## Slide 10
Authentication System
Secure User Access with Firebase Auth
Authentication Methods
📧 Email & Password Registration / Login
— Secure hashed credentials via Firebase Auth
🌐 Google OAuth Integration
— One-tap sign-in with existing Google account
🍎 Apple Sign-In (Placeholder)
— Cross-platform support for iOS users
🔑 OTP Verification
— 4-digit code sent to email for verification
🔄 Password Reset Flow
— Forgot password → Email link → New password
Screens Flow
→ Splash Screen (auto-auth check)
→ Onboarding (4-page carousel)
→ Sign Up / Sign In
→ OTP Verification
→ Forgot / New Password
→ Home (Drone Dashboard)
Backend: Firebase Authentication + Cloud Firestore State: AuthCubit (BLoC pattern) with sealed states DI: GetIt service locator for auth repository
10/24

## Slide 11
Onboarding & Splash
First-Time User Experience
Animated Splash Screen
• Phoenix logo animation with fade-in + scale • SVG-based logo rendering • Automatic auth check on startup • Routes to Onboarding or Home accordingly
4-Page Onboarding Carousel
• Page 1: Saving Lives — Mission statement • Page 2: Thermal Scanning — AI detection • Page 3: Stay Connected — Real-time data • Page 4: Every Second Counts — Call to action • Interactive PageView with dot indicators
Implementation Details
• BlocSelector for efficient rebuilds • Skip/Next/Start buttons with state management • SVG assets stored as embedded base64 • Page snap physics for natural feel
Key Metrics
• Total screens: 10 (auth + onboarding + drone)
• Routing: GoRouter with declarative config
• State management: BLoC/Cubit pattern
• Screen adaptation: flutter_screenutil
• Theme: Professional dark-first design
11/24

## Slide 12
Live Video Streaming
MJPEG over WebSocket with Multi-Mode Display
Video Pipeline
Drone Camera
→
TCP Socket
→
FastAPI Server
→
WebSocket Broadcast
→
Flutter App
NORMAL MODE
Standard RGB video feed from drone camera with no image processing
THERMAL MODE
Simulated thermal imagery using 5×5 color filter matrix for heat mapping
AI OVERLAY
YOLO detection bounding boxes + confidence scores overlaid on video
WebSocket Client: 3 concurrent channels (video/detection/command) | DroneWsBridge converts raw streams to domain events
12/24

## Slide 13
AI Overlay & HUD
Real-Time Detection Visualization
On-Screen Overlay Elements
• Bounding Boxes — Colored rectangles around detected persons
• Confidence Scores — Percentage label above each box
• Human Count — Live counter in top corner
• Grid Pattern — Custom GridPainter overlay for spatial reference
• Gradient Overlay — Transparent gradient for readability
• Status Bar — Connection status + telemetry strip
AI Overlay Technical Stack
Detection Data (JSON from WebSocket):
{
"detections": [
{
"label": "person",
"confidence": 0.92,
"x": 0.45, "y": 0.32,
"w": 0.12, "h": 0.28
}
],
"human_count": 3
}
Rendering: Custom AiDetectionOverlay widget
with CustomPainter for bounding boxes
13/24

## Slide 14
GPS Tracking & Mapping
Real-Time Drone Position on OpenStreetMap
Map Features
• OpenStreetMap Integration via flutter_map
• Real-time drone marker with red pin
• User location marker with blue dot
• Path history — polyline track of drone movement
• Auto-follow: camera centers on drone position
• Responsive tile loading with caching
Data Source
GPS Coordinates published to Firestore: drone/location → {lat, lng, timestamp} DroneTrackingCubit subscribes to real-time Firestore stream with 10s disconnect timer
Map Screen Components
• MapScreenHeader — Greeting + connection status
• DroneMapView — Map controller + state handling
• DroneMapStatusBar — Battery/Temp/Signal row
• MissionStatusCard — Pre-completed missions count
• StartMissionButton — Gradient action button
14/24

## Slide 15
Telemetry Monitoring
Real-Time Drone Health & Status Dashboard
75%
BATTERY
Remaining power level
3
HUMANS
Detected persons
42m
ALTITUDE
Height above ground
8.5 m/s
SPEED
Current travel speed
38°C
TEMP
System temperature
Connection Status & Reports
• ConnectionStatusBar — Green/Red dot indicator • DroneStatusCard — Summary card with circular indicators + mini map • ReportsSection — Real-time incident feed with timestamps • Report types: Human Detected, System Overheated, Mission Complete
Data Source: Firestore real-time stream from drone/status DroneStatusCubit manages telemetry state Automatic disconnection detection (10s timer)
15/24

## Slide 16
Virtual Joystick
Touch-Based Drone Control Interface
Joystick Capabilities
• Full-screen immersive touch interface
• Custom JoystickPainter with gradient thumb
• Directional indicators around the thumb
• Normalized output (x, y) for drone commands
• Tap-to-toggle visibility of controls overlay
• Gesture-based pan with smooth tracking
Command Mapping
WebSocket Command Format:
{"cmd": "move", "data": {"x": 0.5, "y": -0.3}}
{"cmd": "start_mission", "data": {}}
{"cmd": "stop_mission", "data": {}}
{"cmd": "land", "data": {}}
Commands written to:
Firestore → drone/commands
WebSocket → /ws/commands
Dual-path ensures reliability:
• Firestore for persistent commands
• WebSocket for low-latency control
16/24

## Slide 17
Mission Management
End-to-End Rescue Mission Lifecycle
1
PLAN
Define mission parameters & search area coordinates
→
2
DEPLOY
Launch drone & establish autonomous flight path
→
3
MONITOR
Real-time video + AI detection + telemetry streaming
→
4
REPORT
Automated incident reports & mission summary logs
→
5
COMPLETE
Return to base mission debrief & data archive
Key Features
• PLAN MISSION button on home screen • Start Mission on map screen • Real-time mission status tracking • Automated incident reports • Mission history and pre-completed mission count • Stop/Land commands for emergency abort • Firebase Firestore for persistent mission data
17/24

## Slide 18
Reports & Alerts
Real-Time Incident Notification System
🚨
Human Detected
AI detection triggered with confidence score and timestamp
🌡
System Overheated
Temperature threshold exceeded warning notification
✅
Mission Complete
Successful mission completion summary report
⚠
Connection Lost
Drone disconnection alert with automatic reconnect timer
Report System Architecture
• Reports stored in Firestore subcollection: drone/reports/entries/{document} • Each report has: type, message, timestamp • ReportsSection widget with empty state • ReportTile with timeAgo formatting • Auto-generated from AI detections & system events
Report Types Implementation: enum ReportType { humanDetected, systemOverheated, missionComplete, connectionLost }
18/24

## Slide 19
UI/UX Design Highlights
Professional Dark Interface for Field Operations
Dark-First Theme
Optimized for outdoor field use with reduced blue light and high contrast readability
Responsive Layout
flutter_screenutil adapts to phones and tablets (base: 393×852)
Smooth Animations
Animated transitions for snackbars, page navigation, state changes
SVG Assets
Custom SVG icons and logo with embedded base64 rendering via flutter_svg
Centralized Theme
AppTheme + AppDimensions for consistent colors, gradients, spacing, and typography
Custom Painters
GridPainter for video overlay, JoystickPainter for controls
19/24

## Slide 20
Architecture & State Management
Clean Architecture with BLoC Pattern
DATA LAYER
Repository Implementations Firebase Auth & Firestore WebSocket Client Dio HTTP Client SharedPreferences
DOMAIN LAYER
Abstract Repositories Entity Models (Equatable) Failure Classes either<Failure, T> patterns
PRESENTATION
Cubits / BLoCs Screens & Widgets Custom Painters State: sealed classes with copyWith
Cubits: OnboardingCubit | AuthCubit | DroneTrackingCubit | DroneStatusCubit | VideoFeedCubit
DI: GetIt service locator • Routing: GoRouter (10 named routes) • Error handling: dartz Either type • ~70+ Dart files across the project
20/24

## Slide 21
Technology Stack
Tools & Technologies Used
MOBILE APP
• Flutter 3.12+
Cross-platform UI framework
• Dart 3.12+
Programming language
• BLoC/Cubit
State management
• GoRouter
Declarative routing
• get_it
Dependency injection
• flutter_map
OpenStreetMap integration
• web_socket_channel
Real-time communication
• flutter_screenutil
Responsive design
BACKEND
• FastAPI
Python web framework
• Uvicorn
ASGI server
• OpenCV
Video processing
• NumPy / Pillow
Image manipulation
• YOLO
AI object detection
• WebSockets
Real-time broadcast
• Firebase Admin
Server-side Firebase
INFRASTRUCTURE
• Firebase Auth
Authentication
• Cloud Firestore
Real-time database
• Firebase Core
Platform initialization
• SharedPreferences
Local storage
• Geolocator
Location services
• google_sign_in
Google OAuth
• dartz
Functional error handling
HARDWARE
• Raspberry Pi
Onboard computer
• Pi Camera v2
Video capture
• NEO-6M GPS
Position tracking
• TCP Socket
Video transmission
• Pi GPIO/UART
Hardware interface
21/24

## Slide 22
Challenges & Solutions
Key Technical Hurdles Overcome
1
Real-Time Video Latency
Optimized MJPEG streaming over WebSocket with frame queue & rate limiting
TCP → Frame Queue → AI Pipeline → WS Broadcast achieved ~15-30 FPS with <500ms latency
2
Disconnection Handling
10-second grace timer before marking drone as disconnected prevents UI flickering
DroneTrackingCubit timer resets on each incoming location update from Firestore
3
Cross-Platform UI Consistency
flutter_screenutil for adaptive layout across phone & tablet with dark-first design
Base design size: 393×852. All dimensions use .w, .h, .r, .sp extensions
4
AI Detection Integration
Custom pipeline with fallback dummy detector for testing without real drone hardware
Abstract detection interface allows swapping YOLO model or using simulated data
5
Firebase Real-Time Sync
Multiple Firestore streams for location, status, reports & commands with error handling
Each stream independently error-handled with Either pattern for clean state
22/24

## Slide 23
Future Enhancements
Roadmap & Next Steps
Real YOLO Model Training
Train custom YOLO model on SAR-specific dataset for higher accuracy in rescue scenarios
Raspberry Pi Hardware Scripts
Complete onboard firmware for autonomous drone control & data relay to laptop server
Multi-Drone Support
Simultaneous operation of multiple drones with individual control interfaces
Offline Mode
Local caching of video & telemetry data for operation in remote areas without internet
Advanced Mission Planning
GPS waypoint plotting & autonomous path planning with obstacle avoidance
Push Notifications
Alert first responders when human detection is triggered or system warnings occur
Flight Recording & Replay
Record missions for post-flight analysis and training purposes
Web Dashboard
Browser-based monitoring interface for command center operations
23/24

## Slide 24
Thank You
Questions & Discussion
Phoenix — Drone Search & Rescue System Project ResQer
Mahmoud Dahy | github.com/mahmoud-dahy | Computer Engineering - Graduation Project 2025/2026
24/24